## Slide 1
Université de Genève
SES - Département des Systèmes d’Information
Infrastructure de
Communication
420426
Prof. Dimitri Konstantas
(UNI Dufour, Bur. 405, tel: 379.7659)
Mr. Alfredo Villalba
(Uni Dufour, Bur. 407 tel: 379.7662)

## Slide 2
Reference Book
Resaux (Computer Networks)
Andrew Tanenbaum
4/e, Pearson Education
Auxiliary book
Computer Networks – A Systems Approach
Larry Peterson & Bruce Davie
2/e Morgan Kaufmann

## Slide 3: Course organization
TP are obligatory
  1/3 of final mark (2 points)
  Valid for both sessions
Final Exam (obligatory!  )
  Open book
  3 hours

## Slide 4: Course WWW site
http://dokeos.unige.ch
  Inscrivez-vous
http://cui.unige.ch/OSG
  Materiel additionel

## Slide 5: Introduction
Chapter 1

## Slide 6: Uses of Computer Networks
  Business Applications
  Home Applications
  Mobile Users
  Social Issues

## Slide 7: Business Applications of Networks
A network with two clients and one server.

## Slide 8: Business Applications of Networks
The client-server model involves requests and replies.

## Slide 9: Home Network Applications
Access to remote information
Person-to-person communication
Interactive entertainment
Electronic commerce

## Slide 10: Home Network Applications (2)
In peer-to-peer system there are no fixed clients and servers.

## Slide 11: Home Network Applications (3)
Some forms of e-commerce.

## Slide 12: Mobile Network Users
Combinations of wireless networks and mobile computing.

## Slide 13: Network Hardware
Local Area Networks
Metropolitan Area Networks
Wide Area Networks
Wireless Networks
Home Networks
Internetworks

## Slide 14: Broadcast Networks
Types of transmission technology
Broadcast links
Point-to-point links

## Slide 15: Broadcast Networks (2)
Classification of interconnected processors by scale.

## Slide 16: Local Area Networks
Two broadcast networks
(a) Bus
(b) Ring

## Slide 17: Metropolitan Area Networks
A metropolitan area network based on cable TV.

## Slide 18: Wide Area Networks
Relation between hosts on LANs and the subnet.

## Slide 19: Wide Area Networks (2)
A stream of packets from sender to receiver.

## Slide 20: Wireless Networks
Categories of wireless networks:
System interconnection
Wireless LANs
Wireless WANs

## Slide 21: Wireless Networks (2)
(a) Bluetooth configuration
(b) Wireless LAN

## Slide 22: Wireless Networks (3)
(a) Individual mobile computers
(b) A flying LAN

## Slide 23: Home Network Categories
Computers (desktop PC, PDA, shared peripherals
Entertainment (TV, DVD, VCR, camera, stereo, MP3)
Telecomm (telephone, cell phone, intercom, fax)
Appliances (microwave, fridge, clock, furnace, airco)
Telemetry (utility meter, burglar alarm, babycam).

## Slide 24: Network Software
Protocol Hierarchies
Design Issues for the Layers
Connection-Oriented and Connectionless Services
Service Primitives
The Relationship of Services to Protocols

## Slide 25: Network Software Protocol Hierarchies
Layers, protocols, and interfaces.

## Slide 26: Protocol Hierarchies (2)
The philosopher-translator-secretary architecture.

## Slide 27: Protocol Hierarchies (3)
Example information flow supporting virtual communication in layer 5.

## Slide 28: Design Issues for the Layers
Addressing
Error Control
Flow Control
Multiplexing
Routing

## Slide 29: Connection-Oriented and Connectionless Services
Six different types of service.

## Slide 30: Service Primitives
Five service primitives for implementing a simple connection-oriented service.

## Slide 31: Service Primitives (2)
Packets sent in a simple client-server interaction on a connection-oriented network.

## Slide 32: Services to Protocols Relationship
The relationship between a service and a protocol.

## Slide 33: Reference Models
The OSI Reference Model
The TCP/IP Reference Model
A Comparison of OSI and TCP/IP
A Critique of the OSI Model and Protocols
A Critique of the TCP/IP Reference Model

## Slide 34: Reference Models
The OSI reference model.

## Slide 35: Reference Models (2)
The TCP/IP reference model.

## Slide 36: Reference Models (3)
Protocols and networks in the TCP/IP model initially.

## Slide 37: Comparing OSI and TCP/IP Models
Concepts central to the OSI model
Services
Interfaces
Protocols

## Slide 38: A Critique of the OSI Model and Protocols
Why OSI did not take over the world
Bad timing
Bad technology
Bad implementations
Bad politics

## Slide 39: Bad Timing
The apocalypse of the two elephants.

## Slide 40: A Critique of the TCP/IP Reference Model
Problems:
Service, interface, and protocol not distinguished
Not a general model
Host-to-network “layer” not really a layer
No mention of physical and data link layers
Minor protocols deeply entrenched, hard to replace

## Slide 41: Hybrid Model
The hybrid reference model to be used in this book.

## Slide 42: Example Networks
The Internet
Connection-Oriented Networks: X.25, Frame Relay, and ATM
Ethernet
Wireless LANs: 802:11

## Slide 43: The ARPANET
(a) Structure of the telephone system.
(b) Baran’s proposed distributed switching system.

## Slide 44: The ARPANET (2)
The original ARPANET design.

## Slide 45: The ARPANET (3)
Growth of the ARPANET (a) December 1969. (b) July 1970.
(c) March 1971. (d) April 1972. (e) September 1972.

## Slide 46: NSFNET
The NSFNET backbone in 1988.

## Slide 47: Internet Usage
Traditional applications (1970 – 1990)
E-mail
News
Remote login
File transfer

## Slide 48: Architecture of the Internet
Overview of the Internet.

## Slide 49: ATM Virtual Circuits
A virtual circuit.

## Slide 50: ATM Virtual Circuits (2)
An ATM cell.

## Slide 51: The ATM Reference Model
The ATM reference model.

## Slide 52: The ATM Reference Model (2)
The ATM layers and sublayers and their functions.

## Slide 53: Ethernet
Architecture of the original Ethernet.

## Slide 54: Wireless LANs
(a) Wireless networking with a base station.
(b) Ad hoc networking.

## Slide 55: Wireless LANs (2)
The range of a single radio may not cover the entire system.

## Slide 56: Wireless LANs (3)
A multicell 802.11 network.

## Slide 57: Network Standardization
Who’s Who in the Telecommunications World
Who’s Who in the International Standards World
Who’s Who in the Internet Standards World

## Slide 58: ITU
Main sectors
  Radiocommunications
  Telecommunications Standardization
  Development
Classes of Members
  National governments
  Sector members
  Associate members
  Regulatory agencies

## Slide 59: IEEE 802 Standards
The 802 working groups. The important ones are marked with *. The ones marked with  are hibernating. The one marked with † gave up.

## Slide 60: Metric Units
The principal metric prefixes.